Viller Hsiao
F9 Microkernel ktimer

---
Agenda
- Concept about operation system time subsystem
- F9 Microkernel ktimer introduction

---
Concept about Operation System Time Subsystem

---
OS Time Subsystem
- Current Time
  - System time, UTC/GMP time, … etc
- Alarm, the time event
- Process timeslice
- Timeout
- Time delay

---
System Time and Tick
- “System time represents a computer system's notion of the passing of time.“
  “System time is measured by a system clock, which is typically implemented as a simple count of the number of ticks that have transpired since some arbitrary starting date, called the epoch.”
  ~ from WIKIPEDIA

---
How Is Tick Implemented?
- Hardware time device
  - Assert interrupt after a programmable inteval
    - Handling tick stuff in timeout Interrupt Service Routine (ISR)
  - Two types
    - Incremental: ARMv7A generic timer
    - Counting down: STM32F4DISCOVERY SYSTICK

---
How Is Tick Implemented? (cont.)
- Timeout ISR
  - Increase system ticks
  - Execute handler of timeout event
  - Re-schedule if required

---
Time Diagram of Ticks
event2
event1
event3
event4
Timer
interrupt
CPU
activities

---
Where Is the Problem?
- Context switch overhead
- Unecessary Power consumed
- Tick resolution
  - Performance, power v.s. timer precision

---
Solution: Tickless
event2
event1
event3
event4
Timer
interrupt
New
CPU
activities
Previous
CPU
activities

---
Example: Linux Timer Subsystem
- Device level
  - Clock source
    - jiffies
  - Clock event
- Hrtimer
- Tickless
  - CONFIG_NO_HZ

---
F9 Microkernel ktimer Introduction

---
Features
- System time
- Time event
- Tickless

---
Configurations
- CONFIG_KTIMER_HEARTBEAT
  - HW cycles per ktimer tick
- CONFIG_KTIMR_MINTICKS
  - Minimum ktimer ticks unit for time event
- CONFIG_KTIMER_TICKLESS
  - Enable tickless

---
ktimer Event Utility
- ktimer_event_create
  - Arguments
    - Timeout ticks
    - Timeout handler
    - Pointer to arguments for timeout handler
  - Return Non-zero to reschedule event again
    - Freed automatically if not be re-scheduled

---
Anotomy
- System time
  - ktime_now
- ktimer event list
  - event_queue
  - Managed by ktable

---
Anotomy (Cont.)
- Life cycle of time event
  - One-shot
  - Continuous
  - Controlled by return value of handler

---
Anotomy (Cont.)
- HW Timer ISR
  - __ktimer_handler()
    - Increase tick
    - Arrange Softirq for handling timer events

---
Anotomy (Cont.)
- HW timer softirq handler
  - ktimer_event_handler()
    - Find timeout event and executing its handler
    - Re-insert event if required

---
Anotomy (Cont.)
- Tickless
  - Enter tickless right before going to CPU idle state
  - Set interval of next timer interrupt as delta of next event
    - Or KTIMER_MAXTICKS
  - Adjust system time after wake up

---
Q & A

---
THE END